DRI3000
Status and Discussion
Keith Packard
Intel Open Source Technology Center
keithp@keithp.com

---
Discussion Areas
- DRI3 design and status
- Present status
- Synchronization between X and DRM
- Present Redirection

---
DRI3 Requirements
- Share DMA bufs as X pixmaps
- Share synchronization objects
- Provide access to correct DRM device

---
DRI3 Status
- Finished
  - X Protocol, XCB binding
  - Mesa DRI3 loader, GLX API
  - X server
  - Intel Mesa and 2D driver
- To Do
  - EGL API
  - X server GL loader
- Needs more test cases

---
DRI3 Extension
- Open
  - X server opens DRM device
  - Prepares for rendering
  - Passes resulting FD back to client
  - Can transparently change to using Render Nodes
- PixmapFromBuffer
  - Client creates DRM object
  - Maps to DMABuf
  - Passes DMABuf FD to X server
  - X server creates pixmap referencing same DRM object
- BufferFromPixmap
  - X server maps Pixmap DRM object to DMABuf
  - Passes DMABuf FD to client
  - Client unwraps DMABuf to get DRM object
- FenceFromFD
  - Client allocates anonymous file with a single page containing futex
  - Passes FD to X server
  - X server maps file and creates an XSyncFence object pointing at it.

---
Present Extension
- PresentPixmap
  - Provide new content for window in a pixmap
- PresentNotifyMSC
  - Returns current media counters in an event
- PresentSelectInput
  - Selects for Present events
- PresentIdleNotify
  - Event sent when pixmap is free for re-use
- PresentConfigureNotify
  - Event sent when window size changes
- PresentCompleteNotify
  - Event sent when PresentRegion operation completes

---
PresentPixmap
- Parameters:
  - serial – client-provided number returned in matching PresentCompleteNotify
  - valid-area – Region of pixmap containing correct pixels
  - update-area – Region of pixmap containing changed pixels
  - x-off, y-off – offset within window for operation
  - wait-fence – SyncFence which blocks execution
  - options – Set of flags to control execution
  - target-msc, divisor, remainder – parameters defining display time
  - options – cut-through, force copy
  - List of window/serial to notify
- Supports vblank synchronized sub-window updates.
- Allow flips even for small updates
- Separate out completion event from buffer idle event

---
Previous “PresentRegion”
- What's in git today
- No 'wait_fence'
  - Requires implicit synchronization between DRM client and X server
- 'idle_fence'
  - See discussion on dealing with idle buffers
- No options
  - force applications to support flipping
- No list of window/serial for notification
  - Needed for redirection

---
XCB changes
- FD passing
  - use recvmsg everywhere
  - Stick incoming Fds in reply structure
- “Special” event queues
  - Split off Present events to special queue
  - Bump pointer to integer to make checking for events cheap (and Mesa compatible)

---
Media Stream Counters
- Monotonic frame counter
- Challenges:
  - Switching monitors
  - DPMS off
  - Suspend/resume
  - VT switch
- Current design
  - Pick a counter for each window
  - Create a fake counter as needed
  - Per-window counter is offset from underlying counter
  - Counters adjusted on transition
- Not working with DPMS/suspend yet
  - events queued to kernel never happen
  - redesign to ignore queued events
- How fast should the fake counter run?
  - Thinking about 1Hz?

---
Present Status
- First protocol version finished
  - Initial protocol, XCB and Xlib bindings
  - Mesa loader, GLX API, various GL/GLX extensions
  - X server DIX
  - Intel Mesa, 2D driver
- Second protocol proposal
  - Adds wait-fence
  - Adds options
- To Do
  - Add more synchronization
  - Add redirect
  - Think about YUV?

---
DRM SyncFences
- Currently implemented with futexes
  - X/DRM details are hidden in video driver
- Not select/poll friendly
  - X server cannot be awoken when fence is signaled via futex API.

---
SyncFence adventures
- Original design included per-pixmap idle fence
- Client wants to wait for any idle fence
- Current implementation guesses which is likely to become idle.
- Can cause deadlocks
- Need to wait for one of a set of fences somehow
- Plan to use events instead of fences

---
Present Redirection
- Busy implementing simplest possible plan
  - Effectively forward PresentPixmap request and let compositor sort it out.
- Want more complicated mechanism (I think)
  - Over-allocate to page-align
  - What about auto-painting window manager frames?